## Slide 1
NDTwin Network Digital Twin
The Manual, Proven End to End
— and what one unstated build flag is worth
Adam · 2026-09-03

## Slide 2
OUTLINE
1
The manual
installed from the public document, in a clean room
pp. 4–6
2
What the experiments say
one build flag = 8× · capacity depends on flow count · 18 papers
pp. 7–17
3
Engineering, and what's next
the traffic round · a criterion that measured the wrong thing
pp. 18–23
2

## Slide 3
WHERE WE LEFT OFF
three written on 27 August · one asked for since
THE ASK
TEST SET IN ADVANCE
TODAY
THE MANUAL
install from the public document, clean room
ANSWERED
§1 · and the site is open in the next tab
DOES MERGE MOVE THE WALL
the 1-in-8 cell's loss moves, or it does not
ANSWERED
72 cells ran — the criterion could not see the wall (p. 19)
FAST BUILD DEFAULT
the L0–L4 suite passes on the fast build
IN PART
install and provenance verified · the suite has not run
THE BOOT RING
arms to 0/6–0/8 on the fixed build
NOT RUN
deliberately deprioritised · carried forward as written
3

## Slide 4
SECTION 1
The manual
Installed from the public document in a clean room — the site itself is the demo
4

## Slide 5
1 · THE MANUAL
IT INSTALLS, AND IT RUNS
clean-room VM · every command as printed
31
installation steps run verbatim — zero non-zero exit codes
12/12
hosts reach each other on the fabric the manual builds
29/29
documented API endpoints exist, with the right methods
7
checks pass on the optional fast build — the debug install untouched
16 s
for the whole stack to converge, on a real clock
12
routes with no page — 29% of the HTTP surface
→ the manual itself, live
5

## Slide 6
1 · THE MANUAL
WHAT RUNNING IT FOUND
defects the document could not show · four fixed, two open
THE MANUAL
grep for the wrong error string · an undocumented interactive prompt · “wait 60 s” measured 80
THE PROGRAM
a second proxy wrote rules before noticing the port was taken · the lock API accepted malformed requests
A GREEN CHECK
“model matches fabric: 4 hosts” printed over 128 — it compares the model with the model
A PHANTOM ROW
a queued, unprogrammed request served as a flow-table row · visible at t = 0 only, on both planes
STILL OPEN
the Ubuntu Server variant · twelve undocumented routes, one of them called by the shipping GUI
The last two are system defects — found by running the document, not by reading it.
doc/2026-08-30_manual-verification-report.md (798f9f5) · FINDING-01 and FINDING-03 at 569f976 · fixes at 89c1754, e29424e, dff87f9.
6

## Slide 7
SECTION 2
What the experiments say
One unstated build flag, a capacity that depends on flow count, and eighteen papers that state neither
7

## Slide 8
2 · WHAT THE EXPERIMENTS SAY
COST PRE-REGISTERED
effect +0.530 s, inside the registered 0.4–0.6 s band
BENEFIT POST-HOC
not registered before the data was read — an observation, not a result
8

## Slide 9
2 · WHAT THE EXPERIMENTS SAY
The ceiling was the access layer; BMv2's is real
THE FOUR SHORT BARS
ECMP hashed onto the top four — not a capacity floor
WHAT 53.1 IS
an interface-counter rate · 32 TCP flows · one link's ECMP share · host CPU 98.7%
9

## Slide 10
2 · WHAT THE EXPERIMENTS SAY
Capacity is a function of flow count
UDP
the ladder is iperf3 -u and “clean rate” is read from loss — this is a UDP claim
THE CONTROL
same path on TCP: T(16)/T(1) = 1.222 and 1.108 — no collapse
10

## Slide 11
2 · WHAT THE EXPERIMENTS SAY
One plane holds its cap; the other collapses below it
UDP, BOTH PLANES
both ladders are iperf3 -u -l 1400 · with TCP the collapse does not appear
SO THE CLAIM IS
“UDP collapses ≈10×”, not “BMv2 collapses”
11

## Slide 12
2 · WHAT THE EXPERIMENTS SAY
Same data, two units, sixteen times apart
THE AMBIGUITY
packet rate moves 1.25× while bit rate moves 16× — Mbit/s without a packet size is a 16× hole
12

## Slide 13
2 · WHAT THE EXPERIMENTS SAY
18 PAPERS, AND WHAT THEY REPORT
12 of them measure BMv2 · counted, not estimated
reporting dimension | of the 12 | note
reports a throughput number | 10 / 12 | two measure latency only
states build flags | 0 / 12 | the variable worth 8× here
runs a build comparison | 0 / 12 | 
names the BMv2 variant | 3 / 12 | all from one lab lineage
states the version | 1 / 12 | 
sweeps packet size | 0 / 12 | 
uses flow count as a variable | 0 / 12 | 
THE GAP
the one variable we measured at 8× is the one none of them state — in our sample of 18
doc/2026-08-29_bmv2-performance-study.md §2-1 at b2cd6b5. Every negative is a statement about these 18 papers and the search boundary in §5-4 — not about the literature.
13

## Slide 14
2 · WHAT THE EXPERIMENTS SAY
Twelve papers, nine reporting dimensions
THE GAPS ARE THE DATA
column totals are asserted against the survey table — a drift crashes the plot rather than drawing it
14

## Slide 15
2 · WHAT THE EXPERIMENTS SAY
Twelve headline numbers, one axis
A THIRD CANNOT BE PLACED
4/12 publish no bit-rate headline · 1/12 is a working point, not a ceiling
NOTHING WAS CONVERTED
a packets-per-second headline stays in packets per second
15

## Slide 16
2 · WHAT THE EXPERIMENTS SAY
Self-reported throughputs span ~2,500×
FOR SCALE
~0.57 Mbit/s to ~1.4 Gbit/s · one build flag on one machine is worth 8× of that
16

## Slide 17
2 · WHAT THE EXPERIMENTS SAY
Known is not the same as reported
DESK CHECK
sources read, not re-measured · BMv2's own page says the debug build is slow, and two papers cite it
AND STILL
neither states its own build · build flags stated: 0/12
17

## Slide 18
SECTION 3
Engineering, and what's next
The traffic round, a criterion that measured the wrong quantity, and what the next report will carry
18

## Slide 19
3 · ENGINEERING, AND WHAT'S NEXT
The criterion never measured the quantity its name says
NOT READ OUT
SATURATED fired 0 times in 72 cells · all four arms right-censored · indistinguishable, not equal
THE FLAT LINE MISLEADS
twin ÷ truth reads 1.009 at the rung that destroys 87–89% of the traffic
BATCHING NOT ESTIMABLE
batch on/off is aliased with leg and time of day — a confound, not noise
19

## Slide 20
3 · ENGINEERING, AND WHAT'S NEXT
THE TRAFFIC ROUND
six arms · registered before any data
IT DISCRIMINATES
the flow endpoint went 8 → 12 under load and tracked the churn — the gate held on both arms
CONTRACT
39/39 against the live kernel, plus a 52-check self-test
THE 128-HOST EXAMPLE
the manual's own worked example passes as printed
THE HALF NOT ASKED
the timing question is unanswerable at 128 hosts — one sample costs 735 ms and needs 500
AND NOT BY SAMPLING HARDER
the instrument is slower than the thing it measures · answered at 4 hosts instead
PREREG 5cbd672, written before any data; kernel 1208d22, rebuild byte-identical. One sample = three endpoints, of which all_destination_paths is 699 ms and 931 KB.
20

## Slide 21
3 · ENGINEERING, AND WHAT'S NEXT
WORTH WRITING UP?
asking, not arguing
QUESTION
Has anyone quantified what an unstated build flag costs?
MEASURED
one build flag · 8.0× on a single hop · 12× across three
MEASURED
unit ambiguity adds 16× on the same data
SURVEYED
0/12 state that flag, in our sample of 18
DESK CHECK
so a ~2,500× spread has no attributable cause — from reading, not measured
THE QUESTION
we did not find anyone who has done this · a pointer would be the useful answer
Not that this is unknown — that being known has not made it reported.
21

## Slide 22
PLANNED FOR THE NEXT REPORT
three, each with the test that settles it
1
Measure the ceiling with a criterion that can see it
SATURATED never fired in 72 cells, so the arms cannot be told apart.
Done when a registered criterion reads out a rung the data plane actually fails at.
2
Finish the third question on its own terms
The fast build's install and provenance are verified. The functional suite is not.
Done when the whole L0–L4 suite passes on the fast build.
3
Close the manual line to publishable grade
Install, whole-stack and API page are green. Four executable pages remain.
Done when every executable page has been executed.
Same shape as the 20 and 27 August pages, so the next report can be checked against this one.
22

## Slide 23
WHERE IT STANDS
settled · open
SETTLED
OPEN
The manual installs
clean room · 12/12 up
The API page
29/29 correct
One build flag
8.0× · 12× across three hops
Units
1.25× or 16×, by choice of unit
Capacity
a function of flow count (UDP)
The survey
0/12 state build flags
The sampling ceiling
measured fidelity, not the wall
Fast build as default
L0–L4 has not run
Manual, remaining
four executable pages
The boot ring
arms never taken to 6–8
Batching
aliased with time of day
Undocumented routes
twelve · one used by the GUI
Marked items are what the next report answers.
23