## Slide 1
Liveness: how the twin decides a bmv2 switch is alive
Two independent kinds of evidence, and a verdict that is allowed to come back “cannot tell”
GATHERED BY THE PROXY
p4_client.probe() — every 2 s
GetForwardingPipelineConfig with COOKIE_ONLY: the cheapest request P4Runtime has,
and a real answer from the switch. → probe_ok, probe_age_s
an LLDP beacon arrives
packet_in with reason = LLDP, recorded unconditionally rather than
only when the edge is new. → last_lldp_age_s
GET /p4/switch_state — evidence, not a verdict
the kernel polls this and decides — nothing above this line changes
DECIDED BY THE KERNEL
probe_ok is absent or not a boolean
no probe of this switch has completed yet
yes
UNKNOWN
Reporting Down here would mark the whole fabric dead for the first seconds of every run.
no
probe_ok == true
an RPC was round-tripped
yes
UP
The only signal that proves a bmv2 process is serving. gRPC channel state was rejected: it sits in IDLE until something forces a connection.
no
probe_age_s > 15 s
kProbeStaleSeconds — the last probe result is stale
yes
UNKNOWN
The proxy’s poller has stalled. That is a fact about the poller, not about the switch.
no
last_lldp_age_s ≤ 12 s
kLldpFreshSeconds — a beacon arrived after the probe failed
yes
UNKNOWN
bmv2 can answer control-plane RPCs while forwarding badly, and a loaded switch can miss one deadline while forwarding well. Fresh beacon against failed probe is a disagreement, not a verdict.
no
DOWN — asked, and nothing else disagreed
Four ways to fail to know, and only one way to be told a switch is dead.
Up → setVertexUp
Down → setVertexDown
Unknown → the graph is not touched

## Slide 2
Failover: what turns a missing beacon into a new route
bmv2 raises no link-down signal, so the absence of a packet the proxy sent itself is the only evidence there is
Beacon out — every 5 s
TopologyManager sends one LLDP frame out of every port of every switch, as a packet_out.
Beacon in
The neighbour’s pipeline sends it to the CPU port. It arrives as packet_in with reason = LLDP,
and stamps the arrival time of that one link direction.
Watchdog pass — every 5 s
now − last beacon > 15 s ?
Three missed beacons. A link that has never spoken at all gets 30 s instead.
Why three and not one. One interval of tolerance would report a failure every time a scan landed just before a beacon did — and a flapping link report is worse than a slow one, because each one tears the edge out of the graph and recomputes every path.
no
yes
The link’s belief flips to down, and the kernel is told
POST /ndt/link_failure_detected, retried on every following pass until the kernel accepts it — a kernel
that happened to be restarting would otherwise cost the notification permanently.
every inbound link of that switch went quiet, and probe_ok is still true ?
Then this is a switch-level symptom, not a link failure — report it, but leave its links in the routing graph.
yes
reported, not rerouted
The one measured failure mode. Taking a bmv2 interface down stalls that switch’s whole packet-in path, so every link into it falls silent at once — one real break produced five down directions, three of them healthy links whose beacons simply had nowhere to be delivered. Reporting may over-report safely; reprogramming may not.
no
install_initial_routes() — reprogram first
BFS over the graph with the down endpoints removed, so a reinstall cannot recompute the same route
back into the broken link. insert_ipv4_route falls back to MODIFY, so the pass is idempotent.
push_destination_paths() — announce second
POST /ndt/inform_all_destination_paths. The kernel’s own pull runs every 60 s, so this only buys latency.
The order is the point. The push advertises the routes that are installed, so announcing first would publish a snapshot that is honest and already out of date — and the corrected one would not arrive until the next transition.
Detection costs between the timeout and the timeout plus one scan — 15 to 20 s by the constants, 10.7 to 14 s measured. Which of those two is right is not yet settled, and tuning the timer before it is would leave us unable to say what moved.