## Slide 1
The P4 proxy agent, module by module
Eight files. One of them talks to the switches, two of them talk to the kernel, and one holds all the state.
NDTwin Kernel
/ndt/* HTTP API · sFlow collector on UDP 6343 · unchanged by this work
Ryu-compatible REST
the kernel polls, unmodified
/ndt/ push — switch entered, link failure and recovery, destination paths
sFlow v5, synthesised — straight into the collector on UDP 6343
P4 proxy agent · FastAPI / uvicorn
main.py
Startup.
Opens all ten switch
connections at once,
builds every box on
this page, and wires
the callbacks between
them.
345 lines
api_routes.py
The only door in.
/v1.0/topology/* · /stats/flowentry/*
/stats/flow/<dpid> · /p4/*
366 lines
ryu_topology.py
338 lines
ryu_flow_stats.py
190 lines
}
Shape only, no state.
They turn the graph into
the exact JSON Ryu
would have returned.
kernel_notifier.py
Northbound push.
The four /ndt/ calls
Ryu used to make.
184 lines
link events, paths
topology_manager.py
All of the state. The networkx graph, BFS routing, the LLDP beacon sender and its watchdog,
and the translation from a Ryu flow rule into a P4 table entry.
1516 lines
reads state, installs rules
p4_client.py
One per switch. P4Runtime gRPC, the clone session, and the split of
every packet_in on its reason field.
755 lines
route writes · LLDP beacons out
reason = LLDP
sflow_emitter.py
Builds a datagram byte-compatible
with what OVS sends.
448 lines
reason = sample
P4Runtime gRPC — one connection per switch
Emulated network (Mininet) — bmv2 simple_switch_grpc × 10
setting/…Topology*.json
Read by the emitter for its agent
addresses and by the kernel for the
same graph. An address the kernel
does not recognise becomes
telemetry attributed to nothing.
Nothing above the kernel line
changes. The proxy answers in
Ryu's shapes and manufactures
the telemetry bmv2 never sends.
Line counts are current file sizes at cc249c8, not diff counts.